## Slide 1: Setting up PLCE webbing
Contents

## Slide 2: Contents
What is PLCE?
History of PLCE
PLCE Versions
Complete Webbing set & component index
Setting up webbing
Further Webbing Equipment
Contents

## Slide 3: What is PLCE?
Personal Load Carrying Equipment (PLCE) is the current tactical webbing system of the British Army.
It consists of a Belt, Yoke (shoulder harness) and a number of Pouches.
Associated with PLCE Webbing is a series of other similar load carrying equipment and rucksacks.
Contents

## Slide 4: History of PLCE (I)
PLCE replaced 58 Pattern webbing, which was made of olive canvas: this system was outdated by the 1980’s. It was very heavy, uncomfortable and shrank when wet- these problems were well noted by soldiers during the 1982 Falklands War.
The US introduced Nylon M-67 (and later ALICE (All-purpose Lightweight Individual Carrying Equipment, )) type webbing during the Vietnam War to overcome the issues associated with canvas in damp climates.
Following their lead, Britain developed 72-Patt webbing, which was based on 58-Patt in nylon. This had very limited use, and was not on general issue.
Contents

## Slide 5: History of PLCE (II)
Developments resumed with the introduction of the SA80 Rifle in the mid-late 80’s. Experimental (85-Patt) PLCE appeared at this time. It was very similar to the first Issue PLCE, but used snaps for closure on all pouches.
The first PLCE (90-Patt) appeared around 1988, in OG. The original type used ’58 pattern C-Hooks for belt attachment, and angled D-Rings for Yoke attachment on the Ammo pouches (so there were separate left and right pouches).
The first production Utility Pouches had additional belt attachments for high mounting, like the ammo pouches of '37 or '44 Pattern webbing.
Contents

## Slide 6: History of PLCE (III)
Newer OG webbing has ambidextrous Yoke fittings and standard PLCE belt attachments. The Disruptive Pattern Material (DPM) version (95-Patt/Soldier 95) has been made since about 1992.
The original concept for PLCE was modular. Known as CEFO (Combat Equipment, Fighting Order) the minimum rig was two Double Ammo Pouches, known as CEFO-AO (Assault Order).
To this, Canteens, Respirators, Entrenching Tools and Bayonets could be added.
Contents

## Slide 7: PLCE Versions
Two primary versions of PLCE Webbing exist: OG (90-Patt) and DPM (95-Patt).
A series of minor modifications to buckles, clips and fastenings also exist within these two versions, dependant on the year of manufacture.
  1: OG only: two types of ammo pouch - left and right. Ammo pouches are internally divided, providing enough space for two magazines per pouch. Pouch fasteners are pull tag type.
  2: DPM and OG: Two types of ammo pouch - left and right. No internal pouch dividers in ammo pouch. Pouch fasteners are pull tag type.
  3: DPM and OG: As 2, but pouch fasteners are replaced with quick release clips.
  4: DPM only. Double pouch – pouches are now side specific, can be used on left or right side. No internal dividers. Semi-directional yoke fastening 'D' rings on pouches have been replaced by universal slotted 'A' rings, which also now appear (in pairs) on Utility Pouches as well.
  5a: DPM only: Single ammo pouch. Pull tag type pocket fastener. Other specification as 4a.
  5b: DPM only: Single ammo pouch. Quick release clips. Other specification as 4a.
Contents

## Slide 8: Complete Set
Requirements:
1 x Yoke
1 x Belt
1 x Utility pouch
1 x Water bottle pouch
2 x Ammo pouches
Contents

## Slide 9: Components: Belt
Buckle LHS (fixed)
Quick Release clip
Buckle (adjustable)
Locator slots
Webbing loops
This way up!
Contents

## Slide 10: Components: Yoke
To ammo pouches
(strap 3)
Ladder lock buckle (A-C)
Webbing Loops
Mesh backing
To ammo pouches (strap 2)
To belt loops
(strap 1)
2
2
1
1
3
3
A
A
B
B
C
C
Contents

## Slide 11: Components: Ammo pouch (I)
Quick Release fastenings
Pull tag fastenings
Contents

## Slide 12: Components: Ammo pouch (II)
Slotted ‘A’ Rings
Webbing belt loops
Belt locator pins
Webbing belt fixing loops
Stud fastenings
Stud Fastening
Contents

## Slide 13: Components: Utility & Water bottle pouch
Back of pouch setup as ammo pouches
Utility Pouch
Water bottle Pouch (90 & 95 Patt)
Contents

## Slide 14: Putting it together
This short guide will show you how to put the webbing together
    Belt
    Fitting the yoke
    Preparing pouches
    Suggested positioning
    Pouch positioning
    Fixing Pouches (a)
    Fixing Pouches (b)
    Fitting the yoke (a)
    Fitting the yoke (b)
    Testing & checking
Contents

## Slide 15: Putting it together (I)
1. Belt
  Hold belt around your waist with two ‘D’ rings at the back held equidistant from spine
  Fasten QR clip at front
  Adjust to fit
  You may need to move belt locator pins on LHS to a new position to ensure QR clip is central.
Setup Index

## Slide 16: Putting it together (II)
2. Fit Yoke (Part 1)
  Lay yoke down on floor, with strapping facing upwards
  Pass yoke belt straps (strap 1) through belt
  Thread Strap 1 through the ladder lock buckles A & B (follow red dotted arrow)
A
1
1
2
2
B
A
B
Setup Index

## Slide 17: Putting it together (III)
3. Prepare Pouches
  Undo stud fastenings, lift webbing fixing loops & belt locator pins so they are pointing upwards and do not infer when threading the belt through the webbing loops
Setup Index

## Slide 18: Putting it together (IV)
4. Suggested positioning
  Suggested pouch positioning is:
Double
Ammo
Pouch
Utility
Pouch
Water
Bottle
Pouch
Double
Ammo
Pouch
Yoke
1
1
2
2
A
A
C
B
Setup Index

## Slide 19: Putting it together (V)
5. Position Pouches
  Slide all pouches into position, ensuring that belt passes through BOTH belt loops on the reverse of the pouches
1
1
2
2
Setup Index

## Slide 20: Putting it together (VI)
6. Fixing pouches
  Insert belt locator pins into belt.
1
1
2
2
Setup Index

## Slide 21: Putting it together (VII)
7. Fixing pouches
  Close webbing loops over locator pins and fasten down using studs.
  Repeat process on each pouch
1
1
2
2
Setup Index

## Slide 22: Putting it together (VIII)
8. Completing yoke
  Thread strap 2 through the ‘A’ clip closest to the Yoke.
  Thread this back through ladder lock buckle B
1
1
B
B
A
A
2
2
Setup Index

## Slide 23: Putting it together (IX)
9. Completing yoke
  Thread strap 3 through the outermost ‘A’ clip.
  Thread this back through ladder lock buckle C on the yoke
C
3
C
3
Setup Index

## Slide 24: Putting it together (X)
10. Testing & checking
  Try on webbing
  Close front QR buckle
  Buddy up, and get them to tighten all ladder lock buckles accordingly
Setup Index

## Slide 25: Further Webbing Equipment
Hip Pad / Hippo Pad
200-rd Minimi Pouch
Entrenching Tool Pouch
Respirator Pouch
Radio Pouch (349)
Personal-Role Radio Pouch
Pistol Holster
SA80 Bayonet Frog
Wire-Cutter Frog
Rifle Grenade Pouch
Strap utility
Contents